## Slide 1: Lab 8 pipeline

## Slide 2: Simple operation with pipeline
Mode0: in_1 * in_2
Mode1: in_3 + in_4
Mode2: in_1 * in_2 * in_3 * in_4
Think twice before writing code

## Slide 3: pipe.sv
Input Signal | Bit Width | Definition
clk | 1 | 4 ns
rst_n | 1 | Asynchronous reset when reset negedge, all output should be zero
in_1 | 6 | Value:0~63, won’t stop until pattern over.
in_2 | 6 | Value:0~63, won’t stop until pattern over.
in_3 | 6 | Value:0~63, won’t stop until pattern over.
in_4 | 6 | Value:0~63, won’t stop until pattern over.
mode | 2 | 0 or 1 or 2, choose calculate mode
in_valid | 1 | High until all inputs are given
Output Signal | Bit Width | Definition
out_valid | 1 | High until all answers are done.
out_value | 27 | Output answer

## Slide 4: Spec
Top module name : PIPE (File name: PIPE.sv)
All output signal should be reset (=0) after the reset signal is asserted.
01_RTL PASS
02_SYN result cannot include any error and latches.
After synthesis, your slack in timing report should be MET
03_GATE PASS
You must use pipeline. Since clock is 4ns.
After output done , output signal should be zero.

## Slide 5: Output & Waveform
Waveform
In_valid and out_valid pull high continuously

## Slide 6: Command
N Y C U . E E , Hsinchu, Taiwan
VLSI Signal Processing Lab.
tar -xvf ~dcsTA01/Lab08.tar
Upload
  cd 09_upload
  ./01_upload
  ./02_download demoX
DEMO1 : 5/2 17:30:00
DEMO2 : 5/3 23:59:59